## Slide 1
Pattern Detection
in Energy Consumption
What we found in the GoiEner cooperative dataset
Gonçalo Rosa · ISCTE-IUL · MSc Data Science · 2025
Supervisors: Prof. Ana Maria de Almeida · Prof. Diana Mendes

## Slide 2
The Data
19,709
users retained
(from 25,559 original)
8 years
hourly readings
2014 – 2022
3
municipalities
northern Spain
80.7 %
residential users
(Household production)
Three cities
▸ Vitoria-Gasteiz · Donostia/San Sebastián · Pamplona/Iruña
▸ All in the Basque Country / Navarra region
▸ All GoiEner cooperative members (same tariff structure)
▸ Selected: ≥ 100 active meters every day, < 10 % gap days
Quality filtering
▸ 25,559 raw smart meters in source
▸ 5,850 excluded: failed imputation or > 5 % missing
▸ 19,709 retained for all analyses
▸ Dominant tariff: p1 – p2 (residential, 90.8 %)
▸ COVID periods: pre / in / post — used throughout

## Slide 3
What the Data Shows — Seasonal & Trend Structure
Household seasonality
▸ Moderate, predictable daily cycle
▸ Seasonal strength Fs ≈ 0.46 – 0.49
▸ Peaked during COVID lockdowns (0.489)
▸ — routines became more regular
▸ Returned near pre-COVID after restrictions
Public buildings
▸ Near-perfect daily regularity
▸ Seasonal strength Fs ≈ 0.985 – 0.990
▸ Fixed office hours dominate signal
▸ Lockdown disrupted (mean dropped to 0.831)
▸ Opposite COVID effect to households
Trend & Residuals
▸ Mean trend slope ≈ 0 (stable in aggregate)
▸ But: 55 % of users show upward trend post-COVID
▸ (was 36 % pre-COVID)
▸ Residuals consistently heavy-tailed
▸ ≈ 2.2 % extreme events — stable across periods

## Slide 4
User Archetypes — K-Means Clustering (k = 3)
10,015 users present in all three COVID periods · 4 features: seasonal strength, kurtosis, extreme rate, trend slope
Type A
10.7 %
of users
▸ High seasonal regularity (Fs̄ = 0.78)
▸ Strong upward trend
▸ Institutional / commercial premises
▸ Fixed daily schedules
Type B
79.7 %
of users
▸ Moderate seasonality (Fs̄ = 0.46)
▸ Mixed trend — no dominant direction
▸ Mainstream residential users
▸ The GoiEner typical profile
Type C
9.6 %
of users
▸ Low seasonal strength (Fs̄ = 0.21)
▸ Extremely heavy-tailed residuals
▸ Median kurtosis: 123
▸ Vacation properties / storage units

## Slide 5
Forecasting Daily Consumption — N-BEATS Wins
MAPE on held-out test set (Aug 2021 – Jun 2022)
Model
Vitoria-G.
Donostia
Pamplona
Seasonal Naive
12.3 %
10.7 %
9.3 %
SARIMA
74.9 %
13.0 %
14.9 %
SARIMAX
53.0 %
3.2 %
6.2 %
LSTM v2
9.7 %
6.1 %
6.8 %
N-BEATS v2 ★
5.3 %
3.4 %
4.4 %
11 models tested across 5 families (baselines, SARIMA, LSTM, N-BEATS, Hybrid)
Validation
▸ 100 bootstrap seeds
▸ Trimmed mean (drop top/bottom 5 %)
▸ N-BEATS v2: MAPE 3.71 – 5.20 %
▸ σ ≤ 0.20 pp — very stable
Why N-BEATS?
▸ Most consistent across all 3 cities
▸ No structural assumptions about series
▸ Residuals fed into anomaly detection

## Slide 6
Anomaly Detection — Ensemble of 5 Algorithms
Approach
▸ N-BEATS residuals (actual − forecast) as anomaly signal
▸ 5 detectors: rolling z-score, Isolation Forest, LOF,
▸ One-Class SVM, K-Means
▸ Calibration prior: 2.2 % extreme-residual rate
▸ (observed across 19,709 users)
▸ Flag a day only if ≥ 3 of 5 detectors agree
0.7 – 1.4 %
ensemble anomaly rate
per city
What we found: December 2021
▸ Anomaly cluster across all 3 cities simultaneously
▸ Residuals almost all positive:
▸ actual consumption above forecast
▸ Timing matches Omicron wave emergence
▸ and renewed social restrictions
▸ (Basque Country / Navarra)
▸
▸ Most likely cause: people staying indoors
▸ → higher residential electricity demand
▸
▸ Caveat: cold weather in December would
▸ produce the same pattern — cannot
▸ separate without temperature records

## Slide 7
Key Takeaways
19,709 users
after quality filtering — dataset is clean and well-structured for analysis
Clear seasonal patterns
daily cycle is the dominant structure; COVID lockdowns made it more regular
3 consumption archetypes
institutional (10.7 %), mainstream residential (79.7 %), intermittent (9.6 %)
N-BEATS best forecaster
MAPE 3.71 – 5.20 % across cities, stable over 100 bootstrap seeds
0.7 – 1.4 % anomaly rate
ensemble of 5 detectors — few enough to review; December 2021 cluster is real
Gonçalo Rosa · goncalo662001@gmail.com · ISCTE · 2025